## Slide 1: Processor Design
CS 161: Lecture 1
1/28/19

## Slide 2: Processors: From the View of a Terrible Programmer
Source code
Compilation
addq %r11, %r12
movq 8(%rbx), %r9
cmpq %rax, %rbx
Machine instructions
A HARDWARE MAGIC OCCURS
Letter “m”
Drawing
of bird
ANSWERS

## Slide 3: Processors: From the View of a Mediocre Programmer
RAM
IP
Instruction to execute
ALU
Registers
Devices
Program instructions live in RAM
IP (“instruction pointer”) register points to memory address of next instruction to fetch and execute
Arithmetic logic unit (ALU)
  Inputs are register values
  Performs operation on inputs (e.g., add, divide)
  Writes result to output register or memory address
Some instructions cause devices to perform actions
Registers versus RAM
  Registers are orders of magnitude faster for ALU to access (0.3ns versus 120ns)
  RAM is orders of magnitude larger (a few dozen registers versus GBs of RAM)
Register size defines the “-bit” part of a CPU
  Ex: 64-bit architectures have 64-bit-large registers

## Slide 4: Instruction Set Architectures (ISAs)
ISA defines the instructions and registers which hardware presents to software
  A compiler translates high-level source code (e.g., C++, Go) to the instructions for a target processor’s ISA
  The processor directly executes ISA instructions
Example ISAs
  ARMv8.2-A: 64-bit ISA popular on smartphones and embedded devices
  x86-64: 64-bit ISA popular on desktop, laptops, and servers; known to cause sadness among programmers and hardware developers

## Slide 5: ISAs: The Three Basic Instruction Types
Arithmetic/bitwise logic
  Ex: Multiply two register values and store result in a third register
  Ex: Left-shift a register value by 2 bits
Data movement between registers and/or memory
  Ex: Store a register’s value into memory
  Ex: Load a memory value into a register
Control flow
  Ex: Unconditionally jump to a particular instruction
  Ex: Jump to an instruction if a register has a value of 0
  Ex: Call a function

## Slide 6: RISC vs CISC: ISA Wars
CISC (Complex Instruction Set Computer)
  A single instruction often does many things
  Instructions are often variable-size to minimize RAM usage
  CISC instructions make life easier for compiler writers, but much more difficult for hardware designers—complex instructions are hard to implement and make fast
x86 is the classic CISC ISA

## Slide 7: RISC vs CISC: ISA Wars
CISC (Complex Instruction Set Computer)
  A single instruction often does many things
  Instructions are often variable-size to minimize RAM usage
  CISC instructions make life easier for compiler writers, but much more difficult for hardware designers—complex instructions are hard to implement and make fast
x86 is the classic CISC ISA
//Copy %rax register’s val to %rbx
mov %rax, %rbx
//Copy *(%rsp+16) to %rbx
mov 16(%rsp), %rbx
//Copy %rbx register val to *(%rsp+8)
mov %rbx, 8(%rsp)
mov instruction: Operands can both be registers, or one register/one memory location

## Slide 8: RISC vs CISC: ISA Wars
if(cpu_direction_flag == 0){
*(%rdi++) = *(rsi++);
}else{
*(%rdi--) = *(%rsi--);
}
//Copy %rax register’s val to %rbx
mov %rax, %rbx
//Copy *(%rsp+16) to %rbx
mov 16(%rsp), %rbx
//Copy %rbx register val to *(%rsp+8)
mov %rbx, 8(%rsp)
CISC (Complex Instruction Set Computer)
  A single instruction often does many things
  Instructions are often variable-size to minimize RAM usage
  CISC instructions make life easier for compiler writers, but much more difficult for hardware designers—complex instructions are hard to implement and make fast
x86 is the classic CISC ISA
mov instruction: Operands can both be registers, or one register/one memory location
//movsb: Copy 1 byte from one
// pointer to another
//%rdi: Destination pointer
//%rsi: Source pointer
if(cpu_direction_flag == 0){
*(%rdi++) = *(%rsi++);
}else{
*(%rdi--) = *(%rsi--);
}
A single hardware instruction has to do:
  a condition test
  a memory read
  a memory write
  two register increments or decrements
That’s a lot!
if(cpu_direction_flag == 0){
*(%rdi++) = *(%rsi++);
}else{
*(%rdi--) = *(%rsi--);
}
Notes: [Note that in movsb, the source and destination pointers are hardcoded into the instruction itself.]

## Slide 9: RISC vs CISC: ISA Wars
RISC (Reduced Instruction Set Computer)
  Each instruction does a simple thing
  Instructions are fixed-sized (or at least easy decode)
  Load/store architecture: all instructions but loads and stores manipulate registers
  RISC ISAs make it easier to design fast, power-efficient hardware
Ex: MIPS, ARM
//On MIPS, operands for mov instr
//can only be registers!
mov a0, a1 //Copy a0 register value
//to a1
//In fact, mov is a pseudoinstruction
//that isn’t in the ISA! Compiler
//translates the above to:
addi 0, a0, a1 //a1 = a0 + 0
RAM is cheap, power efficiency is important, and RISC makes it easier to design fast CPUs—so who cares if compilers must work a little harder to compile code?

## Slide 10: x86-64: Registers
16 general-purpose integer registers
  %rbp: break pointer
  %rsp: stack pointer
  %rax, %rbx, %rcx, %rdx, %rsi, %rdi, %r8, %r9, %r10, %r11, %r12, %r13, %r14, %r15: used for various purposes
%rip: instruction pointer (i.e., holds the address of the next instruction to execute)
  Incremented or decremented by more than one instruction during jumps, function calls/returns
Various special-purpose registers like:
  %cr3: the page table pointer
  %xmm0—%xmm15: floating point registers

## Slide 11: x86-64: System V Calling Convention
int64_t foo(int64_t a, int64_t b,
int64_t c, int64_t d,
int64_t e, int64_t f,
int64_t g, int64_t h){
int64_t local0 = a*b*c;
int64_t local1 = d*e*f;
return local0 - local1;
}
Simplest case: callee arguments+retval are integers or pointers
  Caller stores first six arguments in %rdi, %rsi, %rdx, %rcx, %r8, and %r9
  Remaining arguments are passed via the stack
  Callee places return value in %rax
a
b
c
d
e
f
%rdi
%rsi
%rdx
%rcx
%r8
%r9
g
h
return addr
saved %rbp
local0
local1
%rsp
%rbp
Caller info
Notes: System V was one of the first commercial versions of the Unix operating system. The design of Unix was extremely influential on subsequent operating systems like Linux. [Reference: https://en.wikipedia.org/wiki/UNIX_System_V]
Note that, if a stack-passed integer argument is smaller than 64 bits, the argument is rounded up to 64-bits in size before being placed on the stack.

## Slide 12
int64_t foo(int64_t a, int64_t b,
int64_t c, int64_t d,
int64_t e, int64_t f,
int64_t g, int64_t h){
int64_t local0 = a*b*c;
int64_t local1 = d*e*f;
return local0 - local1;
}
a
b
c
d
e
f
%rdi
%rsi
%rdx
%rcx
%r8
%r9
g
h
return addr
saved %rbp
local0
local1
%rsp
%rbp
Caller info
Caller-saved regs
  %rdi%, %rsi, %rdx, %rcx, %r8, %r9, %r10, %r11, %rax
  Can be overwritten by callee, so if the caller wants to preserve their value, must do so *before* invoking callee
Callee-saved regs
  %rbp, %rbx, %r12, %r13, %r14, %r15
  Assumed by caller to *not* be modified by callee, so callee must push old values on the stack *before* updating these registers
//Code at start of function.
//Save old breakpointer.
pushq %rbp
movq %rsp, %rbp
//Assume that function needs
//to overwrite callee-saved
//%rbx and %r12.
pushq %rbx
pushq %r12
//Allocate local vars.
subq $0x10, %rsp
//Rest of function . . .
Notes: If we look at the bottom of the diagram, we see that the first six arguments for the callee are stored in %rdi, %rsi, %rdx, and so on. This is why these registers are *caller* saved---the caller has to stash the old values in these registers before using the registers to pass arguments to the callee.

## Slide 13: How can a processor efficiently execute instructions?

## Slide 14: Pipelining: The Need for Speed
Vin Diesel needs more cars because VIN DIESEL
A single car must be constructed in stages
  Build the floorboard
  Build the frame
  Attach floorboard to frame
  Install engine
  I DON’T KNOW HOW CARS ARE MADE BUT YOU GET THE POINT
Q: How do you design the car factory?

## Slide 15: Factory Design #1
Suppose that building a car requires three tasks that must be performed in serial (i.e., the tasks cannot be overlapped)
Further suppose that each task takes the same amount of time
We can design a single, complex robot that can perform all of the tasks
The factory will build one car every three time units
t=0
t=1
t=2

## Slide 16: Factory Design #2
Alternatively, we can build three simple robots, each of which performs one task
The robots can work in parallel, performing their tasks on different cars simultaneously
Once the factory ramps up, it can make one car every time unit!
t=1
Car 1
Car 0
t=0
Car 0
t=3
Car 3
Car 2
Car 1
t=2
Car 2
Car 1
Car 0
The factory has ramped up: the pipeline is now full!

## Slide 17: Pipelining a Processor
Executing an instruction requires five steps to be performed
  Fetch: Pull the instruction from RAM into the processor
  Decode: Determine the type of the instruction and extract the operands (e.g., the register indices, the immediate value, etc.)
  Execute: If necessary, perform the arithmetic operation that is associated with the instruction
  Memory: If necessary, read or write a value from/to RAM
  Writeback: If necessary, update a register with the result of an arithmetic operation or a RAM read
Place each step in its own hardware stage
  This increases the number of instructions finished per time unit, as in the car example
A processor’s clock frequency is the rate at which its pipeline completes instructions

## Slide 18
Processors: From the View of a Master Programmer
ID/EX
EX/MEM
MEM/WB
+
Memory
IP
Addr
Instr
Registers
Read reg0 idx
Read reg1 idx
Write reg idx
Write reg data
Read data 0
Read data 1
Sign extend
imm to 64-bit
Current instruction register
Next sequential IP
ALU
?
Memory
Addr
WrData
RdData
?
Write reg idx
+
Conditions?
Sign-extended imm
Opcode
Instr
size

## Slide 19
//IP=addr of addq instr
//Fetch addq instr, increment
//IP to next instr
ID/EX
EX/MEM
MEM/WB
+
Memory
IP
Addr
Instr
Registers
Read reg0 idx
Read reg1 idx
Write reg idx
Write reg data
Read data 0
Read data 1
Sign extend
imm to 64-bit
Current instruction register
Next sequential IP
ALU
?
Memory
Addr
WrData
RdData
?
Write reg idx
+
Conditions?
Sign-extended imm
Fetch:addq %r8, %r9
Opcode
Instr
size

## Slide 20
//Read reg0=%r8 Read reg1=%r9
//Write reg=%r9
//Opcode=add
ID/EX
EX/MEM
MEM/WB
+
Memory
IP
Addr
Instr
Registers
Read reg0 idx
Read reg1 idx
Write reg idx
Write reg data
Read data 0
Read data 1
Sign extend
imm to 64-bit
Current instruction register
Next sequential IP
ALU
?
Memory
Addr
WrData
RdData
?
Write reg idx
+
Conditions?
Sign-extended imm
Decode:addq %r8, %r9
Opcode
Instr
size

## Slide 21
ID/EX
EX/MEM
MEM/WB
+
Memory
IP
Addr
Instr
Registers
Read reg0 idx
Read reg1 idx
Write reg idx
Write reg data
Read data 0
Read data 1
Sign extend
imm to 64-bit
Current instruction register
Next sequential IP
ALU
?
Memory
Addr
WrData
RdData
?
Write reg idx
+
Conditions?
Sign-extended imm
Execute:addq %r8, %r9
//Calculate read data 0 +
// read data 1
Opcode
Instr
size

## Slide 22
ID/EX
EX/MEM
MEM/WB
+
Memory
IP
Addr
Instr
Registers
Read reg0 idx
Read reg1 idx
Write reg idx
Write reg data
Read data 0
Read data 1
Sign extend
imm to 64-bit
Current instruction register
Next sequential IP
ALU
?
Memory
Addr
WrData
RdData
?
Write reg idx
+
Conditions?
Sign-extended imm
Memory:addq %r8, %r9
//Nothing to do here; all
//operands are registers
Opcode
Instr
size

## Slide 23
ID/EX
EX/MEM
MEM/WB
+
Memory
IP
Addr
Instr
Registers
Read reg0 idx
Read reg1 idx
Write reg idx
Write reg data
Read data 0
Read data 1
Sign extend
imm to 64-bit
Current instruction register
Next sequential IP
ALU
?
Memory
Addr
WrData
RdData
?
Write reg idx
+
Sign-extended imm
Writeback: addq %r8, %r9
//Update %r9 with the
//result of the add
Opcode
Conditions?
Instr
size

## Slide 24: A NEW INSTRUCTION ARRIVES

## Slide 25
//IP=addr of mov instr
//Fetch mov instr and
//increment IP
ID/EX
EX/MEM
MEM/WB
+
Memory
IP
Addr
Instr
Registers
Read reg0 idx
Read reg1 idx
Write reg idx
Write reg data
Read data 0
Read data 1
Sign extend
imm to 64-bit
Current instruction register
Next sequential IP
ALU
?
Memory
Addr
WrData
RdData
?
Write reg idx
+
Conditions?
Sign-extended imm
Fetch:mov 8(%r10), %r11
Opcode
Instr
size

## Slide 26
//Read reg0=%r10 Write reg=%r11
//Imm=8
//Opcode=mov
ID/EX
EX/MEM
MEM/WB
+
Memory
IP
Addr
Instr
Registers
Read reg0 idx
Read reg1 idx
Write reg idx
Write reg data
Read data 0
Read data 1
Sign extend
imm to 64-bit
Current instruction register
Next sequential IP
ALU
?
Memory
Addr
WrData
RdData
?
Write reg idx
+
Conditions?
Sign-extended imm
Decode:mov 8(%r10), %r11
Opcode
Instr
size

## Slide 27
ID/EX
EX/MEM
MEM/WB
+
Memory
IP
Addr
Instr
Registers
Read reg0 idx
Read reg1 idx
Write reg idx
Write reg data
Read data 0
Read data 1
Sign extend
imm to 64-bit
Current instruction register
Next sequential IP
ALU
?
Memory
Addr
WrData
RdData
?
Write reg idx
+
Conditions?
Sign-extended imm
Execute:mov 8(%r10), %r11
//Calculate the mem addr:
// %r10 + 8
Opcode
Instr
size

## Slide 28
ID/EX
EX/MEM
MEM/WB
+
Memory
IP
Addr
Instr
Registers
Read reg0 idx
Read reg1 idx
Write reg idx
Write reg data
Read data 0
Read data 1
Sign extend
imm to 64-bit
Current instruction register
Next sequential IP
ALU
?
Memory
Addr
WrData
RdData
?
Write reg idx
+
Conditions?
Sign-extended imm
Memory:mov 8(%r10), %r11
//Ask the memory hardware
//to fetch data at addr
Opcode
Instr
size

## Slide 29
ID/EX
EX/MEM
MEM/WB
+
Memory
IP
Addr
Instr
Registers
Read reg0 idx
Read reg1 idx
Write reg idx
Write reg data
Read data 0
Read data 1
Sign extend
imm to 64-bit
Current instruction register
Next sequential IP
ALU
?
Memory
Addr
WrData
RdData
?
Write reg idx
+
Conditions?
Sign-extended imm
Writeback:mov 8(%r10), %r11
//Update %r11 with the
//value from memory
Opcode
Instr
size

## Slide 30: x86-64: Branches
Most arithmetic instructions (e.g., add, sub) set condition flags to 1 if certain conditions are true
  ZF: Result was zero
  CF: Result generated a carry-out
  SF: Result was negative (i.e., sign bit was set)
  OF: Result caused overflow
cmp and test also set flags without updating registers
  cmp %x, %y: Set flags using %y – %x
  test %x, %y: Set flags using %x & %y (i.e., using logical and)
Conditional jump instruction jXXX offset jumps to %rip+offset if certain flag conditions are true
  Ex: jz offset jumps if ZF is set
  Ex: js offset jumps if SF is set
Notes: [References: http://www.cs.tufts.edu/comp/181/x64_cheatsheet.pdf
https://www.felixcloutier.com/x86/jmp]

## Slide 31
//IP=addr of jz instr
//Fetch jz instr and
//increment IP
ID/EX
EX/MEM
MEM/WB
+
Memory
IP
Addr
Instr
Registers
Read reg0 idx
Read reg1 idx
Write reg idx
Write reg data
Read data 0
Read data 1
Sign extend
imm to 64-bit
Current instruction register
Next sequential IP
ALU
?
Memory
Addr
WrData
RdData
?
Write reg idx
+
Conditions?
Sign-extended imm
Fetch:jz $0x40
Opcode
Instr
size

## Slide 32
//If ZF is 1, set next IP to
// IP + signExtend($0x40)
ID/EX
EX/MEM
MEM/WB
+
Memory
IP
Addr
Instr
Registers
Read reg0 idx
Read reg1 idx
Write reg idx
Write reg data
Read data 0
Read data 1
Sign extend
imm to 64-bit
Current instruction register
Next sequential IP
ALU
?
Memory
Addr
WrData
RdData
?
Write reg idx
+
Sign-extended imm
Decode:jz $0x40
Opcode
Conditions?
Instr
size

## Slide 33
ID/EX
EX/MEM
MEM/WB
+
Memory
IP
Addr
Instr
Registers
Read reg0 idx
Read reg1 idx
Write reg idx
Write reg data
Read data 0
Read data 1
Sign extend
imm to 64-bit
Current instruction register
Next sequential IP
ALU
?
Memory
Addr
WrData
RdData
?
Write reg idx
+
Sign-extended imm
Execute:jz $0x40
//Does nothing
Opcode
Conditions?
Instr
size

## Slide 34
ID/EX
EX/MEM
MEM/WB
+
Memory
IP
Addr
Instr
Registers
Read reg0 idx
Read reg1 idx
Write reg idx
Write reg data
Read data 0
Read data 1
Sign extend
imm to 64-bit
Current instruction register
Next sequential IP
ALU
?
Memory
Addr
WrData
RdData
?
Write reg idx
+
Sign-extended imm
Memory: jz $0x40
Opcode
//Does nothing
Conditions?
Instr
size

## Slide 35
ID/EX
EX/MEM
MEM/WB
+
Memory
IP
Addr
Instr
Registers
Read reg0 idx
Read reg1 idx
Write reg idx
Write reg data
Read data 0
Read data 1
Sign extend
imm to 64-bit
Current instruction register
Next sequential IP
ALU
?
Memory
Addr
WrData
RdData
?
Write reg idx
+
Conditions?
Sign-extended imm
Writeback: jz $0x40
Opcode
//Does nothing
Instr
size

## Slide 36: The Problem with Branches
We don’t know if a branch is taken until the end of the decode stage . . .
. . . which means that the fetch stage may have fetched the wrong instruction!
lbl:
cmpq %r8, %r9
jz lbl
subq %r10, %r11
. . .
movq 8(%r9), %r12
t=1
jz
cmpq
t=2
subq
jz
cmpq
t=0
cmpq
IF
ID
EX
MEM
WB
We don’t know whether we should branch until the end of t=2 . . .
. . . so we don’t know whether movq should have been fetched until end of t=2!
jz lbl
cmpq %r8, %r9
subq %r10, %r11
Notes: The cmpq instruction has to perform an arithmetic operation to determine which condition flags to set. So, the conditions flags can’t be tested by the jz instruction until the end of the cycle in which the cmpq instruction executes. The reason is that the output of the cmpq has to travel along the wire that goes from the ALU to the “conditions” oval.

## Slide 37: The Problem with Branches
One solution: Processor automatically inserts a nop after each branch
  A nop (“no operation”) does not change the processor’s state
  So, executing a nop never affects correctness (although it does slow down the program due to a wasted processor cycle)
lbl:
cmpq %r8, %r9
jz lbl
subq %r10, %r11
. . .
movq 8(%r9), %r12
At beginning of t=3, IF uses output of ID from t=2 to fetch the appropriate instruction
t=1
jz
cmpq
t=2
nop
jz
cmpq
t=0
cmpq
IF
ID
EX
MEM
WB
t=3
nop
jz
cmpq
subq or
movq

## Slide 38: The Problem with Branches
Modern processors use table-driven branch prediction
  Key: Address of a branch instruction
  Value: Prediction about whether the branch will be taken
When ID encounters a branch, ID consults the table to determine whether to feed IF the next sequential IP or the jump target
CORRECT PREDICTION
t=1
jz
cmpq
t=0
cmpq
IF
ID
EX
MEM
WB
When EX encounters a branch:
  EX resolves the branch test and updates the prediction table
  Flushes the pipeline and resets IP if the previous prediction was wrong
t=2
jz
cmpq
subq or
movq
ID consults table and sets IP appropriately
No need for a pipeline bubble!

## Slide 39: The Problem with Branches
t=3
nop
jz
cmpq
Right
instr
Modern processors use table-driven branch prediction
  Key: Address of a branch instruction
  Value: Prediction about whether the branch will be taken
When ID encounters a branch, ID consults the table to determine whether to feed IF the next sequential IP or the jump target
INCORRECT PREDICTION
t=1
jz
cmpq
t=0
cmpq
IF
ID
EX
MEM
WB
When EX encounters a branch:
  EX resolves the branch test and updates the prediction table
  Flushes the pipeline and resets IP if the previous prediction was wrong
t=2
jz
cmpq
Wrong
instr
ID consults table and sets IP to the address of the wrong instruction
The error is detected here
Wrong instruction erased