## Slide 1: Intro to Storage Devices and File Systems
CS 161: Lecture 11
3/6/19

## Slide 2: Why Do File Systems Exist?
A storage device is a big, linear array of bytes
Most applications want a higher-level storage abstraction:
  String-based naming of application data (e.g., “koala.jpg” instead of “the bytes between offsets 12,802 and 12,837”)
  Automatic management of storage blocks as files are created and deleted
  Performance optimizations like:
    Caching of recently read/written data
    Prefetching of preexisting data that is likely to be read in the future
  Some notion of reliability in the presence of application crashes, OS crashes, and unexpected power failures

## Slide 4
Platter
R/W heads
Spindle
Notes: Note that the platters are double-sided, i.e., they store data on both sides. Also note that, in commodity hard drives, all of the read/write heads move together, in unison; however, fancier drives can have sets of independently-moving heads. See here: https://www.extremetech.com/computing/260946-seagates-new-multi-actuator-technology-double-hard-drive-speeds

## Slide 5
Cylinder
Cylinder
group
Track
Sector (4KB)
Notes: A sector is the smallest unit of reading and writing. For example, if a disk has a sector size of 4 KB, and you want to read 3 bytes, then you have to read the entire 4 KB sector that contains the 3 bytes. In fact, you might have to read TWO sectors if the bytes that you want to read span two adjacent sectors!
[For a long time, hard disks used a sector size of 512. However, modern disks now use a sector size of 4K. Ref: https://en.wikipedia.org/wiki/Advanced_Format]

## Slide 6: Accessing Data on a Hard Disk: Mechanical Latencies
Seek time: Moving the disk head to the right track
  Laptop/desktop drives have average seek times of 8—15ms
  High-end server drives have average seek times of 4ms
Rotational latency: Moving the target sector under the disk head
  Dependent on the revolutions-per-minute (RPM) of the drive
  RPMs between 5400—7200 typical for laptop and desktop drives; server drives can go up to 15,000
  So, average rotational latencies are 5.56—4.17 ms for laptop/desktop drives, 2 ms for high-end server drive
If you want to read or write an entire cylinder, you just have to pay the seek cost, and then you can read/write the cylinder as the disk rotates

## Slide 7: Your Disk Is Sealed To Prevent Tragedies
[Courtesy of our friends at Seagate]

## Slide 8: Solid-state Storage Devices (SSDs)
An SSD contains blocks made of pages
  A page is a few KB in size (e.g., 4 KB)
  A block contains several pages, is usually 128 KB or 256 KB
To write a single page, YOU MUST ERASE THE ENTIRE BLOCK FIRST
A block will fail after a certain number of erases (~1000 for slowest-but-highest-density flash, ~100,000 for fastest-but-lowest-density flash)
. . .
Page
0
1
2
3
4
5
6
7
8
9
10
11
Block
0
1
2

## Slide 9: Latency of SSD Operations
Read a page: Retrieve contents of entire page (e.g., 4 KB)
  Cost is 25—75 microseconds
  Cost is independent of page number, prior request offsets
Erase a block: Resets each page in the block to all 1s
  Cost is 1.5—4.5 milliseconds
  Much more expensive than reading!
  Allows each page to be written
Program (i.e., write) a page: Change selected 1s to 0s
  Cost is 200—1400 microseconds
  Faster than erasing a block, but slower than reading a page
Hard disk: 4—15ms avg. seek latency
2—6ms avg. rotational latency

## Slide 10
10011110
00100010
01101101
11010011
Block
Page
11111111
11111111
11111111
11111111
00110011
11111111
11111111
11111111
To write the first page, we must first erase the entire block.
Now we can write the first page . . .
. . . but what if we needed the data in the other three pages?

## Slide 11: Flash Translation Layer (FTL)
Goal 1: Translate reads/writes of logical blocks into reads/erases/programs of physical pages+blocks
  Allows SSDs to export the simple “block interface” that hard disks export
Goal 2: Reduce write amplification (i.e., the amount of extra copying needed to deal with block-level erases and garbage collection)
Goal 3: Implement wear leveling (i.e., distribute writes equally to all blocks, to avoid rapid failures of “hot” blocks)
FTL usually implemented by the SSD hardware

## Slide 12: FTL Approach #1: Direct Mapping
Have a 1-1 correspondence between logical pages and physical pages
Reading a logical page is straightforward
Writing a logical page is trickier:
  Read the entire physical block into memory
  Update the relevant page in the in-memory block
  Erase the entire physical block
  Program the entire physical block using the new block value
Logical
pages
Physical
pages
Block
Block
Block

## Slide 13
Sadness #1: Write amplification
  Writing a single page requires reading and writing an entire block
Sadness #2: Poor reliability
  If the same logical block is repeatedly written, its physical block will quickly fail
  Particularly unfortunate for logical metadata blocks

## Slide 14: FTL Approach #2: Log-based mapping
Basic idea: Treat the physical blocks like a log
  Send data in logical-page-to-write to the physical page at the end of the log
  Maintain a mapping between logical pages and the corresponding physical pages in the SSD
As logical blocks are deallocated or overwritten, the associated physical blocks must be garbage collected!
Logical
pages
0
1
2
3
4
5
6
7
8
9
10
11
. . .
pages
0
1
2
3
4
5
6
7
8
9
10
11
Block
0
1
2
Physical

## Slide 15
. . .
Page
0
1
2
3
4
5
6
7
8
9
10
11
Block
0
1
2
Uninitialized
Valid
Log head
Logical-to-physical map

## Slide 16
. . .
Page
0
1
2
3
4
5
6
7
8
9
10
11
Block
0
1
2
write(page=92, data=w0)
Logical-to-physical map
92 --> 0
Log head
erase(block0)
logHead++
program(page0, w0)
1*
1*
1*
1*
w0
Log head
Uninitialized
Valid

## Slide 17
. . .
Page
0
1
2
3
4
5
6
7
8
9
10
11
Block
0
1
2
write(page=92, data=w0)
Logical-to-physical map
92 --> 0
17 --> 1
erase(block0)
logHead++
program(page0, w0)
1*
1*
1*
w0
Log head
write(page=17, data=w1)
program(page1, w1)
logHead++
w1
Log head
Uninitialized
Valid

## Slide 18
. . .
Page
0
1
2
3
4
5
6
7
8
9
10
11
Block
0
1
2
write(page=92, data=w0)
Logical-to-physical map
92 --> 0
17 --> 1
erase(block0)
logHead++
program(page0, w0)
1*
1*
w0
write(page=17, data=w1)
program(page1, w1)
logHead++
w1
Log head
Advantages w.r.t. direct mapping
Avoids expensive read-modify-write behavior: don’t need to erase then program entire block to write a single page
Better wear levelling: writes get spread across physical pages, even if there is spatial locality in writes at logical level
Uninitialized
Valid

## Slide 19
. . .
Page
0
1
2
3
4
5
6
7
8
9
10
11
Block
0
1
2
write(page=92, data=w4)
Logical-to-physical map
92 --> 0
17 --> 1
33 --> 2
68 --> 3
erase(block1)
logHead++
program(page4, w4)
w2
w3
w0
w1
Log head
1*
1*
1*
1*
Log head
w4
92 --> 4
Garbage version of logical block 92!
Uninitialized
Valid

## Slide 20
. . .
Page
0
1
2
3
4
5
6
7
8
9
10
11
Block
0
1
2
Logical-to-physical map
92 --> 0
17 --> 1
33 --> 2
68 --> 3
w2
w3
w0
w1
1*
1*
1*
Log head
w4
92 --> 4
Garbage version of logical block 92!
At some point, FTL must:
  Read all pages in physical block 0
  Write out the second, third, and fourth pages to the end of the log
  Update logical-to-physical map
Uninitialized
Valid

## Slide 21: Trash Day Is The Worst Day
Garbage collection requires extra reads+writes
Overprovisioning makes GC less painful
  SSD exposes a logical page space that is smaller than the physical page space
  By keeping extra, “hidden” pages around, the SSD tries to defer GC to a background task (thus removing GC from critical path of a write)
SSD will occasionally shuffle live (i.e., non-garbage) blocks that never get overwritten
  Enforces wear levelling
Notes: The garbage collection traffic is “extra” because it doesn’t correspond to an IO that was directly issued by an application---instead, the garbage collection traffic is pure bookkeeping overhead.

## Slide 22: SSDs versus Hard Drives (Throughput) [Source: “Flash-based SSDs” chapter of “Operating Systems: Three Easy Pieces” by the Arpaci-Dusseaus]
Device
Random
Reads
Writes
(MB/s)
(MB/s)
Sequential
Reads
Writes
(MB/s)
(MB/s)
Samsung 840 Pro SSD
Seagate 600 SSD
Intel 335 SSD
Seagate Savio 15K.3 HD
103 287 421 384
84 252 424 374
39 222 344 354
2 2 223 223
Dollars per storage bit: Hard drives are order-of-magnitude cheaper!
[SSD: ~$0.50/GB HD: ~$0.035/GB]
Hard drives have terrible random IO performance! The disk head has incurs a seek penalty and rotational delay for most IOs :-(.
SSD random writes are faster than SSD random reads: the SSD can batch writes and then issue them in one burst, but a read can’t complete until the data has actually been fetched.
For sequential IOs, disks are more competitive.
Notes: There are three interesting trends to note:
1) Hard drives have terrible performance for random reads and writes. The reason is that, for random workloads, the disk head is moving all around, incurring a bunch of seek latencies and rotational delays. In contrast, an SSD only has to pay electronic latencies. But, as we see from this chart, a file system for SSDs would also benefit from converting random IOs to sequential ones, because SSDs also have a performance disparity between random and sequential IO.
2) A second interesting trend is that, for SSDs, random writes are faster than random reads. This is because the SSD can batch a bunch of writes, and then write them in one burst to the end of the log. The SSD can’t play those kinds of tricks with reads. Also note that, like a hard disk, an SSD also has a “geometry.” Internally, the SSD groups a bunch of blocks together. Consecutively accessing pages in that group are faster than consecutively accessing pages across many different groups. [For a high-level overview of SSD geometries, see https://www.cactus-tech.com/resources/blog/details/solid-state-drive-primer-8-controller-architecture-channels-and-banks]
3) We see another interesting trend by looking at the sequential numbers. For sequential reads and writes, the performance difference between SSDs and hard drives is much smaller. So, if you’re designing a machine, and you know that the machine will only be running applications with sequential workloads, then maybe you should put a hard disk in the machine instead of an SSD. You’ll get a lot more storage capacity for the same amount of dollars, and your sequential performance will be pretty reasonable. In terms of dollar per storage bit, there’s a 10x differences between hard drives and SSDs. In other words, for a given amount of money, you can buy a hard disk that has ten times more storage than an SSD with the same dollar cost. So, SSDs have roughly twice as fast sequential throughput, but roughly a tenth of the storage capacity of a hard disk.

## Slide 23: Files and Directories
A file is a named, linear region of bytes that can grow and shrink
  Associated with metadata like:
    a user-visible name (e.g., “koala.jpg”)
    a size in bytes
    access permissions (read/write/execute)
    statistics like last modification time
    a seek position if open
  File also has a low-level name (e.g., Linux inode number) that the file system uses to locate the file data on a storage device
  File systems are typically agnostic about the contents of the file (i.e., applications decide how to interpret file bytes)
A directory is a container for other files and directories
  Typically contains pairs of <user-visible-name, low-level-name>
  Nested directories create hierarchical trees (e.g., “/home/todd/photos/koala.jpg”)

## Slide 24: Files as Single Extents (1960s File Systems)
A file’s metadata consists of:
  A starting sector for the file data
  The number of bytes in the file (note that the last sector may not be completely full)
Advantages:
  Simple!
  Metadata is small
  Efficiently supports sequential and random IO
Challenges:
  For a new file, how much space should be pre-llocated?
  What happens if the file needs to grow beyond its allocation, or shrink?
  External fragmentation
Metadata
Contiguous
sectors

## Slide 25: Files as Linked Lists (FAT: MSDOS, SSD memory cards)
Advantages
  Easy to shrink and grow files
  Low internal and external fragmentation
  Calculating sector offsets for sequential IO is easy
Disadvantages
  Sequential IO requires a lot of seeks
  Random IO is difficult—where does the target sector live?
  Must store pointer information at the end of each data block
=

## Slide 26: Files as Collections of Extents (IBM OS360, ext4)
Advantages:
  If extents are large, then sequential IO almost as fast as with a single extent
  Random IO almost as efficient as with single extent (offset calculations a little trickier)
  Metadata is small
Challenges:
  How large should a file’s initial extents be?
  What happens if a file needs to grow or shrink?
  External fragmentation not as bad, but depending on design, may have internal fragmentation inside each extent
Contiguous
sectors
. . .
. . .

## Slide 27: Files as Flat Indices
Advantages
  Easy to calculate offsets for both sequential and random IO
  Low internal and external fragmentation
Disadvantages
  Maximum file size is fixed by the number of entries in an index
  Sequential IO requires a lot of seeks
=
=
=

## Slide 28: Files as Hybrid Indices (FFS, ext2, ext3)
Top-level index contains direct pointers, indirect pointers, doubly-indirect pointers, etc.
Advantages:
  Efficient for small files: don’t need to materialize indirect blocks
  There is still a maximum file size, but it’s really big
  Low internal and external fragmentation
Disadvantages:
  Reading or writing a single data block may require multiple disk accesses to fetch indirection info
  Even if indirection info is cached, reading or writing adjacent blocks may require extra seeks if those blocks are not physically adjacent on disk

## Slide 29: Free Space Management
Fixed-sized blocks: File systems typically use a bitmap to indicate which blocks are in use
  Allocation metadata is very compact
  Finding a single free block is straightforward . . .
  . . . but finding a *contiguous* region of N free blocks is tedious without auxiliary data structures
Extents: File system can implement “on-disk malloc”
  File system breaks the disk into discrete-sized extents (e.g., 4KB, 8KB, 12KB,…,4MB), or arbitrarily-sized extents sorted by size
  File system maintains a list of unallocated extents
  To allocate an extent for a request of size N bytes, file system uses a policy (e.g., best-fit, worst-fit, first-fit, etc., each of which has trade-offs between internal fragmentation, external fragmentation, and speed of finding a match)